## Slide 1: Building a Locomotion Based Hexapod Application
10305056:Srijit Dutt
09305073:Udaya Kumar
09305063:Venkatesh Velaga

## Slide 2: Agenda
Problem Statement
Task Specification
Project Plan
FSM
Innovation and Challenges
Task Completed
Tasks Planned Initially
Review Test Plan/Cases
Reusability Features
Future Enhancements

## Slide 3: Problem Statement
Making the hexapod to move in all the directions , climbing the obstacles and then to dance. All the three tasks are demonstrated sequentially by our code

## Slide 4: Task Specification
Motion of a Hexapod: It can move in 12 different directions
3 types of gait motion
  2 Tripod gait motion
  Two legged motion
Motion can also be controlled by the keyboard through ZigBee module.
Obstacle Climbing
Dancing: 3 different dancing steps

## Slide 5: Project Plan
Work Division
  Srijit Dutt : Coding
  Uday Kumar: Initial participation for topic selection
  Venkatesh Velga : Documentation and presentation
Task | Date
Survey, Project Topic Selection | 16th Sep
Designing Basic Hexapod Servo Control Routines | 3rd Oct
Different Hexapod Gaits | 10th Oct
Advanced Hexapod Motions, ZigBee Module | 17th Oct
Obstacle Climbing | 24th Oct
Documentation | 7th Nov

## Slide 6: FSM
Hexapod in rest
Moves Forward to some distance
Climbs
Obstacle
Dancing Hexapod
Burn the code 1
Burn Code 2
Control Hexapod using Key pad

## Slide 7: Challenges
Battery Lifetime (Battery lasts about 10min and requires 30-45mins to charge)
Calibration of 18 servos : Different legs move by different angles when given the same movement command
Differences of grip between the various legs of the hexapod

## Slide 8: Innovations
Obstacle Climbing
  The height of the obstacle climbed by the hexapod is comparable to the maximum height the robot can lift it’s body to
Different gaits for different terrain types

## Slide 9: Task Completed
Motion of Hexapod(Completed)
  The problem we faced here is that due to frictional effect the motion is not as expected.
  The solution is we and the other team got the rubbers attached to the bottom of the legs to reduce the friction effect
Obstacle Climbing(Completed)
Dancing(Completed)
The common problem faced during all the three tasks implementation is the battery

## Slide 10: Tasks planned initially
White line following of hexapod
Have not done it because of no white line sensors for hexapod
Obstacle avoidance
Thought that obstacle climbing would be much more challenging to do. And also for obstacle avoidance we need obstacle of large height in order to get it identified by the IR Sensors

## Slide 11: Review, Test Plan/Cases
Burn the code on to hexapod and all the three tasks mentioned above will be executed sequentially
There is another snippet of code which separately demonstrates the controlling of the motion with hexapod.

## Slide 12: Re-usability features
Every task implemented is modular and independent of other tasks
Common functionalities are defined as macros in the header files
Code is made as modular as possible so that on e module can be edited without effecting the other and each module is reusable.

## Slide 13: Future Enhancements
Any new applications on hexapod like obstacle avoidance using web cam
Automatically detect obstacle height and decide whether to climb the obstacle or avoid it
Dance steps of the hexapod can be synchronized to the music beats
Better locomotion algorithm including study of crab and insects gaits